## Slide 1: Imaging Processing

## Slide 2: What is Image Process?
The Image Processing is an electronic form of document filing.
A paper document is passed through a scanner to make a digitized image, then stored on a storage device
It is the process of scan, Crop, Edit, Enhancement and Indexing then stored on a storage device

## Slide 3
Workflow Process

## Slide 4: Key Process
Imaging Process
Scanning
Crop
Edit
Basic Index
Image Enhancement
Full Index

## Slide 5: Scanning Items
Scanning from Paper document
Scanning from book
Scanning from microfilm
Scanning from other classic devices

## Slide 6: Book Scanning

## Slide 7: Microfilm roll scanning

## Slide 8: What is mean by cropping?
Cropping refers to the removal of the outer parts of an image to improve framing, transformation of images and other common scanning defects and corrections It’s a process to re arrange the length and breath of an image

## Slide 10: What does mean by Image Edit
Image editing enclose the processes of altering images such as removal of black border, removal of unwanted vertical and horizontal lines in between the text, removal of unwanted blank pages, identify missing pages and etc, Image editing is known as re-arranging of scanned pages

## Slide 11: Key note of Edit
When Editing be sure all information is legible.
Stamp Dates and Times
Seals
Names
Addresses
Legal Descriptions
Signatures.

## Slide 12: Instructions of crop and edit
Negative Transform
Mirror Horizontal / Vertical
Deskew
Rotate 180, Rotate 90 Right and Rotate 90 Left
Black Border Removal
Darken / Lighten Image
Delete pages
Page number arranged
Masking
Split Images

## Slide 13: Negative Transform
Transform a negative image to positive A positive image is a normal image A negative image is a total inversion of a positive image, in which light areas appear dark and vice versa We needs to edit the image that transform the image from negative to positive image with help of application
Shortcut key=“N”

## Slide 15: Mirror Horizontal and Mirror Vertical
Straighten mirror images A mirror image is a reflected duplication of an object that appears identical but reversed in horizontal We needs to fix the problem and edit such images and bring it to normal view
Shortcut key= H & V

## Slide 18: Deskew
Straighten crooked images, due to high-volume scanners, automatic document feeder inevitably skew paper We needs to fix the problem and obtain straighten images without rescan
Shortcut Key=“D”

## Slide 20: Rotate 180, Rotate 90 Right and Rotate 90 Left
Rotate images, due to high-volume scanners, automatic document feeder inevitably skew paper

## Slide 24: Black Border Removal
Remove black border around images, the black border will be produced due to paper scanner with black background We needs to fix this problem and remove the black border around the images

## Slide 26: Darken / Lighten Image
Balance the light and Darkness of an Image If an image has very less or high contrast and brightness, We needs to adjust the contrast and brightness while doing crop and edit
+ or - symbol

## Slide 27: Delete pages
Delete Pages Delete unwanted pages, and exact duplicate pages

## Slide 29: Masking
Remove grayscale and cleaning images Some of scanning paper copies has grayscale shading We needs to fix the problem and clean the grayscale shading

## Slide 31: Page number arranged
Page number rearranged It there is reversal page numbers or the page number with non sequential order, We needs to rearrange the images as per the pagination

## Slide 32: Split Images
If there is an image with multiple pages, the image needs to be split based on the multiple pages while doing crop

## Slide 34: Image Retakes
Please make sure that when editing all information is legible on Stamp Dates and Times, Seals, Names, Addresses, Legal Descriptions, Signatures and other non editable scanning errors in the image, else it should be flagged as “Retake” with suitable below listed reasons

## Slide 35: Instructions of Image Retakes
Darken Image
Lighten Image
Out of Focus
Bleed Through
Microfilm Retake
Polarity
Notation
Vertical or Horizontal Line Removal
Cut Off
Missing Page
Other Scanner Error

## Slide 36: Polarity
This is a problem where some images have half part of the page with white background and part of the page with black background. We needs to reconvert such images with different backgrounds.

## Slide 37: Polarity Retake

## Slide 38: Notation
A note is typed or written in the margin that surrounds the page (also called as marginalia notation). We will mark such images as “Retake” for reconverting the image.

## Slide 39: Notation Retake

## Slide 40: Vertical or Horizontal Line Removal
Remove lines, horizontal, vertical or both. The line removal is so smart that lines crossed in between the text characters. We needs to flag it as “Retake” for reconverting the page.

## Slide 41
Vertical or Horizontal Line Removal Retake

## Slide 42: Cut Off
A portion of the page appears to be Cut Off or missing. We needs to flag such images as "Retake" for re-converting.

## Slide 43
Cut Off Retake

## Slide 44: Missing Page
If a sequentially numbered image is completely missing, we needs to flag it as “Retake” for finding the image in the original scanned image
page 1, page2, page3, Page5,

## Slide 45: Bleed Through
Reversed text is bleeding through the page. If data and text present on back side of the Image are visible on front side of the image due to transparency. We needs to fix the problem and flag this type of Images as retake for reconverting the image

## Slide 47: Out of Focus /Poor Image
Image is blurry and hard to read. If there is out of focus image where as information is not legible on Stamp Dates and Times, Seals, Names, Addresses, Legal Descriptions and Signatures, We will flag it as “Retake” for reconverting the image.

## Slide 49: Darken and Light Image &
Image is dark all over or any specific area. If there is an illegible darken image which we are unable to adjust contrast and brightness while editing, We will flag this Image as “Retake” for reconverting the image
Image is light all over or any specific area. If there is an illegible light image which we are unable to adjust contrast and brightness while editing, We will flag this Image as “Retake” for reconverting the image

## Slide 50: Image Enhance
Image enhancement is the process of adjusting digital images so that the results are more suitable for display or further image analysis. For example, you can remove noise, sharpen, or brighten an image, making it easier to identify seal or signatures.
Enhancing grayscale images with histogram equalization.
Contrast-limited adaptive histogram equalization

## Slide 51: Indexing
Indexing is the process of describing or classifying a document by index terms or other symbols in order to indicate what the document is about, to summarize its content or to increase its findability. In other words, it is about identifying and describing the subject of documents.
General Indexing fields are
    Book number
    Page number
    Document number
    Document Date
    Granter
    Grantee
    Document type